## Slide 1
测试部：Tessie.Hou
SpectrumWiFi测试分享

## Slide 2
SpectrumWiFi Architecture
01
SpectrumWiFi Traffic Flows
02
SpectrumWiFi WAG Setup
03
Expansions
04
Demo
05

## Slide 3
Architecture

## Slide 4
01
02
03
user authentication process
All EAP messages are encapsulated by hostapd in Radius request and sent over the GRE tunnel.
This ensures that even these trusted control packets remain isolated from the home traffic.
ip address acquisition
The DHCP packets from clients will be transparently bridge at L2 over GRE tunnel to remote DHCP server running on WAG.
Because of transparent bridging both DHCP clients and server will see each other on the same LAN.
internet access
With respect to spectrumwifi, WAG is also the internet access server. In our design, all data traffic from clients will be transparently bridged over GRE to WAG.
Traffic Flows

## Slide 5
Packet Flow
Notes: br-commtap
This is a classic linux software bridge which ensure that all the spectrumwifi related traffic is switched at layer 2 and remain sparate from home traffic.
gre-tap
The layer 2 gretap interface which is used to create layer 2 transparent bridging across WAN and WAG.

## Slide 6
Interface Components
l2 bridge (br-tap / br-com)
gre-tap
pip (veth0/veth1)
vlan (veth1.x)
ip link / ip -6 link
ifconfig
brctl
vconfig
brctl (apt install bridge-utils)
vconfig (apt install vlan)
Interfaces
Commands

## Slide 7
Service Components
AAA
DHCPv4
GRE tunnel
freeradius
isc-dhcp-server
GRE interface
freeradius (apt install freeradius)。
isc-dhcp-server (apt install isc-dhcp-server)。
Services
Application

## Slide 8
ip link add gretap_secr type gretap local 10.8.6.222 remote 10.8.6.176
ip addr add 10.8.6.222/24 dev ens33
brctl addbr br-tap / brctl addif br-tap gretap_secr / brctl addif br-tap veth0
ip link add veth0 type veth peer name veth1
brctl addbr br-com / brctl addif br-com veth1 / ip addr add 12.0.0.2/24 dev br-com
ifconfig veth0 veth1 ens33 br-tap br-com up / ip link set dev gretap_secr up
ip addr show ens33
Interface Configuration
ip -6 link add gretap6_secr type ip6gretap local 2001:db1::2 remote 2001:db1::1
ip -6 addr add 2001:db1::2/64 dev ens33
brctl addbr br-tap / brctl addif br-tap gretap_secr / brctl addif br-tap veth0
ip link add veth0 type veth peer name veth1
brctl addbr br-com / brctl addif br-com veth1 / ip addr add 12.0.0.2/24 dev br-com
ifconfig veth0 veth1 ens33 br-tap br-com up / ip -6 link set dev gretap6_secr up
ip addr show ens33

## Slide 9
freeradius的配置：
添加关联密钥
vim /etc/freeradius/clients.conf
...
client 10.8.6.0/24 {
secret = secret123
shortname = spectrumwifi
}
添加用户密码
vim /etc/freeradius/users
...
“test" Cleartext-Password := “test"
Reply-Message = "Hello, %{User-Name}“
...
Service Configuration
isc-dhcp-server的配置：
绑定监听接口
vim /etc/default/isc-dhcp-server
...
INTERFACES = “br-com”
添加分配网段
vim /etc/dhcp/dhcpd.conf
...
subnet 12.0.0.0 netmask 255.255.255.0 {
range 12.0.0.10 12.0.0.120;
option broadcast-address 12.0.0.255;
option routers 12.0.0.2;
}
...
创建日志文件
touch /var/lib/dhcp/dhcpd.leases

## Slide 10
echo 1 > /proc/sys/net/ipv4/ip_forward
vim /etc/sysctrl.conf
net.ipv4.ip_forward=1
net.ipv6.conf.all.forwarding=1
iptables -A FORWARD -i br-com -o ens33 -j ACCEPT
iptables -A FORWARD -i ens33 -o br-com -m state --state ESTABLISHED,RELATED -j ACCEPT
iptables -t nat -A POSTROUTING -o ens33 -j MASQUERADE
NAT configuration

## Slide 11
01
02
03
04
05
06
SSID VLAN && Uplink VLAN
Support Domain
GRE Keepalive
DHCP Relay
DSCP Marking && ATF
Band Steering && Fast Roaming
拓展延伸
注：del GRE over IPSec
Notes: IPv6 LDRA (IPv6 DHCPv6 relay agent)

## Slide 12
THANK YOU !
感谢聆听